| VESSEL NAME: | DATE: |
| --- | --- |

Weather Decks & Accommodation  (All Ships) :      Note: It is not necessary to physically operate the  equipment. Operability of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Does the physical condition and appearance of the external hull, weather decks , superstructures etc. present a well maintained vessel. (Note: when carrying out initial and pre-registration inspections, Inspectors should examine fore & aft peak tanks and selected ballast tanks, void spaces moon-pools, cement rooms etc to obtain an overview of the vessel's structural condition – accelerated corrosion, buckling, wastage, coating breakdown, anode condition etc. Spaces inspected to be noted;FP, AP, No. 6 wbt etc. ) |  |
| --- | --- |
| Are cargo holds & compartments fit for purpose, including requirements for ventilation & drainage - initial and pre-registration inspections only:,Inspectors should, selectively observe the internals of cargo holds, container fittings & cell guides etc for signs of abnormal wear & tear) |  |
| Is the vessel free from hull, valve or pipeline leakage liable to cause pollution |  |
| Do winches, windlasses & capstans appear to be in good condition & being well maintained - inspect securing devices, brake linings & foundations |  |
| Do mooring wires & ropes appear in good condition & free of joining splices |  |
| Do bits, fairleads, chain stoppers & emergency towing arrangements appear in good condition with freedom of movement & being well greased |  |
| Do cranes & derricks appear in good condition – observe appearance of hydraulic seals, drums, wires, hook, controls, boom rests & boom securing devices |  |
| Is the SWL of cranes & derricks clearly marked on booms |  |
| Do deck pipelines, electrical conduits & fittings appear in good condition, well maintained & free of temporary repairs |  |
| Do watertight doors, port holes, fan flaps, ventilator closures, fire flaps & other closing devices, sounding pipes & air pipes appear in good condition & are they operable |  |
| Are access and closing arrangements of cargo holds & compartments capable of being properly secured & sealed |  |
| Does the fo'c'sle / fore peak bilge bilge alarm operate on the bridge |  |
| Do gangways (incl safety nets), steps & guard rails, stairways, pilot ladders & hoists, appear in good condition with non-slip surfaces as necessary |  |
| Does the deck lighting appear adequate and properly maintained |  |
| Are hull markings correctly placed, legible & in accordance with the vessel’s carving & marking note |  |
| Are Load Lines correctly marked & clearly indicated |  |
| Does the accommodation appear hygienic, well lit, comfortable & tidy |  |
| Are alleyways free of obstruction & emergency exits clearly marked |  |
| Are galleys, pantries, handling spaces & refrigerated spaces clean & tidy |  |
| Are personnel alarms functioning in refrigerated spaces |  |
| VESSEL NAME: | DATE: |

Weather Decks & Accommodation  (All Ships) :      Note: It is not necessary to physically operate the  equipment. Operability of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Other Observations: |  |
| --- | --- |

Page 2 of 2