| VESSEL NAME: | DATE: |
| --- | --- |

Life Saving & Fire Fighting Equipment  (All Ships): Note: It is not necessary to physically operate   equipment. Operability and condition of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Who is the safety officer onboard the vessel |  |
| --- | --- |
| Are safety meetings held periodically Date of last safety meeting ---> |  |
| Are safety signs and other important information displayed in English |  |
| Is the ship’s medical locker equipped in accordance with MN1726 |  |
| Are Muster Lists correctly displayed & in good order |  |
| Are fire control plans displayed within the accommodation areas |  |
| Are SART’s correctly located for rapid deployment in survival craft |  |
| Are lifeboat & liferaft operating instructions displayed |  |
| Do lifeboat hulls and equipment appear in good condition |  |
| Do lifeboat / liferaft launching mechanisms appear in good condition, free of wear, not painted and well greased |  |
| Are lifeboat engines, propulsion gear & steering well maintained & operational |  |
| Are Lifeboats fully equipped with emergency items (ref checklist 32 items - SOLAS Chpt III, IV, Reg 41.8) |  |
| Are lifeboats properly marked with people capacity & ship’s name |  |
| Are life rafts in good condition & service dates in order |  |
| Do life raft hydrostatic release devices appear correctly attached and in good condition |  |
| Are lifeboat engines run on test periodically: Date of last test -------> |  |
| Are lifeboats launched periodically: Date of last launch ---> |  |
| Inspectors are required to witness a boat drill and launching of lifeboats boats |  |
| Do lifebuoys, lifebuoy quick release mechanisms & self activating smoke floats appear in good condition |  |
| Are life jacket donning notices posted |  |
| Do pyrotechnics & line throwing devices appear in good condition, in date and identified by self - illuminating labels |  |
| Are sufficient life jackets on board (including for children if carried) & fitted with whistle & light |  |
| Are the main and emergency fire pumps fully operational |  |
| Inspectors are required to witness remote starting of the emergency fire pump, pressurising of fire main and discharge from furthest deck monitor. |  |
| Are isolating valves in fire & foam lines clearly marked |  |
| Is the International ship/shore connection clearly identified |  |
| Do fire hydrants, hoses & nozzles appear correctly stowed & in good condition |  |
| Do portable extinguishers and appliances appear in good order and in date |  |

| VESSEL NAME: | DATE: |
| --- | --- |

Life Saving & Fire Fighting Equipment  (All Ships): Note: It is not necessary to physically operate   equipment. Operability and condition of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Are manually operated “alarm points” clearly identified |  |
| --- | --- |
| Are breathing apparatus sets and air bottles available ready for immediate use |  |
| Are firemen’s suits & equipment available for immediate use |  |
| Inspectors are required to witness a fire drill |  |
| Does the fixed fire extinguishing system in cargo spaces conform to SOLAS requirements & appear in good condition: Date of last examination --> |  |
| Are operating instructions for fixed fire extinguishing systems clearly posted at fire control points |  |
| Are automatic fire doors and shutters fully operational – Inspectors to sight test records |  |
| In the Galley, do fire control & ventilation measures appear adequate |  |
| Are paint lockers protected by fixed fire fighting systems, fitted with explosion proof lights and provided with “No Smoking Signs” |  |
| Other observations:- |  |

Page 2 of 2