| VESSEL NAME: | DATE: |
| --- | --- |

Machinery & Equipment  (All Ships) : Note: Normally it is not necessary to physically operate equipment. Operability, availability and condition of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Does the main and auxiliary machinery & equipment appear to be fully operational and well maintained |  |
| --- | --- |
| Is an engine room log book in use & signed by Master & C/E |  |
| Are entries in the machinery space oil record book up to date and signed by the Master / Chief Engineer |  |
| Are Chief Engineer’s emergency procedures & standing orders displayed in the ER control room. |  |
| Are pollution prevention procedures displayed in the control room |  |
| Is the fire & general alarm operational – Inspector to witness |  |
| Are machinery failure alarms and safety trips tested periodically – Inspector to sight test records |  |
| In the case of a UMS vessel is the UMS alarm system tested periodically: - Inspector to sight test record. |  |
| Are all ventilation fan dampers operational and tested periodically - Inspector to sight test records & witness the operation of selected dampers |  |
| Are ER skylight closing mechanisms operational and tested periodically. Inspector to sight test records. |  |
| Are bunkering procedures displayed in the engine room |  |
| Do fuel oil pipes and flexible hoses on engines and equipment appear in good condition and free of leaks |  |
| Do lubricating oil handling systems appear free of leaks |  |
| Are hot surfaces that could pose a fire hazard properly insulated |  |
| Is the general housekeeping & cleanliness of engine room, plating, machinery, bilges, stores and workshops to a good standard. |  |
| Do sea water systems appear free of leaks. |  |
| Is the bilge pumping system reported fully operational |  |
| Is the emergency bilge suction valve clearly marked |  |
| Is the OWS operational (sight oil record book) |  |
| Are operating procedures posted in the vicinity of the OWS |  |
| Is the OWS ship side overboard valve locked shut in port |  |
| Are main switchboards, generators and other electrical equipment protected from potential water spray and adequately provided with insulated floor matting |  |
| Are ER lighting levels adequate for safe access / operation |  |
| Do the ER lighting emergency batteries appear in good condition and tested periodically – Inspector to witness operation of lights or sight test records |  |

| VESSEL NAME: | DATE: |
| --- | --- |

Machinery & Equipment  (All Ships) : Note: Normally it is not necessary to physically operate equipment. Operability, availability and condition of equipment may be ascertained by the inspector’s judgement, verbally by ship’s staff, observed from log book entries etc. Inspectors may request sample testing of equipment as considered necessary.

| Inspection Item | Remarks |
| --- | --- |

| Is the emergency generator in a continual state of readiness, fuel tank fully charged and starting instructions clearly displayed |  |
| --- | --- |
| Inspectors are required to witness the starting (by auxiliary hydraulic or battery starter) and excitation of the emergency generator |  |
| Does the electric welding equipment appear in good condition and are operating procedures displayed |  |
| Does the gas welding / burning equipment – hoses & fittings - appear in good condition, correctly stored in ventilated compartments and with operating procedures displayed |  |
| Are the main and auxiliary steering control systems operational |  |
| Is the emergency steering gear tested periodically – Inspector to sight test record |  |
| Inspectors are required to witness operation of main & auxiliary steering systems and the change over and testing of the emergency steering gear. |  |
| Are emergency steering changeover procedures clearly displayed in the steering flat. |  |
| Is the steering gear emergency oil reserve tank fully charged. |  |
| Are communications between steering compt & bridge satisfactory. |  |
| Is the steering compass and the rudder angle indicator clearly visible at the emergency steering position. |  |
| Are suitable gratings and handrails fitted around the steering gear |  |
| Are escape routes clearly marked from all levels in the ER |  |
| Are emergency exit doors accessible & clear of obstructions |  |
| Are machinery space fire doors operational and well maintained |  |
| Are watertight doors correctly marked & operational |  |
| Is the machinery space emergency escape trunk clear & properly equipped |  |
| Other observations:- |  |

###### Page 2 of 2